## Slide 1
Development of Ontological Architecture for Capability-based Co-simulation Configuration
—
Master‘s Thesis, RPTU Kaiserslautern
Anuja Chakraborty, Department of Computer Science
Matriculation number: 425838
E-Mail: vyr58gad@rhrk.uni-kl.de
Presented on July 1st, 2025
Supervised by: Prof. Dr.-Ing. Peter Liggesmeyer & Siwara Schmitt

## Slide 2: Agenda
1. | Introduction
2. | Related Work & Research Gap
3. | Concept Diagram
4. | Implementation
5. | Evaluation & Discussion
6. | Conclusion & Future work

## Slide 3: Introduction
  Research Motivation: Simulation is critical in automotive systems, where multiple subsystems interact via heterogeneous models.
      Key Issues:
      Current co-simulation configuration is manual, error-prone, and hard to scale.
      Ontologies offer formal semantics and reuse potential but existing work lacks a comprehensive layered architecture.
      Research Objective: Design a modular, standards-aligned ontology architecture to enable semantic reasoning, capability matching, and reusable co-simulation configurations.

## Slide 4: Related Work & Research Gap
      Use of TBox, ODPs for modular design to enhance reusability and reduce engineering effort.
      Layered ontology architecture mainly in manufacturing, production, supply chain contexts.
      Ontology-Driven Simulation Frameworks such as DeMO, OSIF, OSMF for semantic interoperability and model discovery.
      No unified ontology framework to integrate simulation models, capabilities, and quality metrics with co-simulation configuration.
      Lack of standardized, domain-independent architecture that can scale across different co-simulation contexts.
      Most work focuses on manufacturing/production; automotive communication networks underexplored.

## Slide 5: Ontological Framework for Capability-based Co-Simulation
Concept Diagram

## Slide 6: Upper-Level Ontology
Concept Diagram
      Integrated BFO (ISO21838) as the foundational semantic framework.
      Leveraged established standards rather than developing new upper-level ontology from scratch.
      Ensures semantic consistency and logical rigor across all ontology levels.
      Key BFO Classes utilized – Function, Object, Process, Quality.

## Slide 7: Mid-Level Ontology
Concept Diagram
      Bridges domain-specific and upper-level abstractions in four-layer architecture.
      Mapped to BFO categories for foundational consistency.
      Integrates concepts from:
        CSS ontology (Capability, Resource, Process)
        VDI 3633 (Simulation)
        IDTA SMT (Provision of Simulation Models)
        ISO 25010 (Quality Attributes)
      Core conceptual structure for capability-based co-simulation configuration.
      Provides classes and properties for domain-level ontologies

## Slide 8: Ontology Architecture as the example of Fraunhofer IESE’s use case AEB
Implementation
Tools and technologies used:
  Protégé: Primary ontology development tool with OWL 2 DL support for visual modeling and reasoner integration.
  Pellet Reasoner: Selected for consistency checking, ontology classification, and complex inferencing.
  Apache Jena Fuseki: SPARQL server for executing semantic queries and competency question validation.

## Slide 9: Domain-Level Ontologies for Fraunhofer IESE
Implementation
      Specializes mid-level structure for simulation models of communication network protocols
      Built for 4 protocols: CAN, Ethernet, FlexRay, LIN based on Fraunhofer FERAL framework specifications.
      Semantic alignment with IDTA SMT "Provision of Simulation Models"
      Each represented as:
        Simulation Model class
        Related Resources (e.g., ECUs)
        Capabilities (e.g., FaultInjection, MessageFrameTransmission)
        Processes and Quality attributes
      Encapsulated using OWL Classes, Object & Data Properties.
      Performed Capability Check Evaluation for simulation models and resource identification.

## Slide 10: Use-case-Level Ontology for Use-case AEB
Implementation
      Real-World Simulation Scenario: Automated Emergency Braking (AEB)
      Aligns with thesis focus on communication protocols in automotive context
      Instantiates domain-level (CAN Bus) concepts to simulate the emergency braking scenario as it involves network of ECUs exchanging sensor/control data over CAN bus.
      Maintains semantic consistency with mid- and domain-level ontologies.
      Enables scenario-specific validation, reasoning, and traceability of simulation model configurations.
      Performed Feasibility Check Evaluation for configuration verification of simulation model instances for required capabilities.

## Slide 11: Capability-based Engineering Approach
Implementation
  Image source: Based on Bock, J. et al. Capabilities, skills and services – CSS model extensions and engineering methodology. Technical report, Platform Industrie 4.0, 2023. Available at: https://www.plattform-i40.de/.

## Slide 12: Evaluation
  Objective: Assess ability of the ontology-based system to configure and validate the simulation models of network protocols for AEB in virtual testbeds.
      Validation Method: Compared ontology-driven configuration to manual expert-built FERAL configuration.
      Outcomes:
      Ontology correctly identified models and associated capabilities fulfilling simulation goals.
      Ontology-derived results matched expert-built FERAL configuration.
      SPARQL queries effectively decomposed complex simulation requirements.
      Significant reduction in manual effort and potential human errors.

## Slide 13: Simulation Goals Definition
  Both goals directly map to formal capabilities (FaultInjection, MessageFrameTransmission) defined in domain ontologies.
      Simulation Goal 1:
      Fault Injection: "Find the effect of network fault injection on emergency braking" - tests system robustness under failure conditions
      Simulation Goal 2:
      Message Frame Transmission: "Measure message frame transmission during emergency braking" - analyzes data integrity and timing between ECUs
Evaluation

## Slide 14: Example Query for Capability Check
Evaluation

## Slide 15: Example Query for Feasibility Check
Evaluation

## Slide 16: Discussion
      RQ1: How can a structured ontology architecture be developed to support capability-based co-simulation configuration?
      Upper-level (BFO), Mid-level (CSS, VDI 3633, ISO 25010, IDTA SMT), Domain-level (protocol-specific), Use-case-level (scenario-specific)
      RQ2: How can simulation models be represented into the ontology architecture to guide capability-based co-simulation configuration?
      Models represented using IDTA SMT "Provision of Simulation Models" with protocol-specific information
      RQ3: How can capabilities and quality attributes be formally incorporated to enable automated configuration?
      CSS:Capability standard for defining capabilities
      ISO 25010-based modeling for Quality attributes
      RQ4: How can communication protocols at the domain level be semantically represented to ensure interoperability in co-simulation?
      FERAL documentation semantics mapped to IDTA SMT standards
      Detailed ontological representations for CAN, LIN, Ethernet, and FlexRay

## Slide 17: Conclusion & Future Work
      Developed a modular, four-layer ontology architecture for semantic co-simulation configuration.
      Successfully aligned multiple industry standards (BFO, VDI 3633, CSS, IDTA SMT, ISO 25010).
      Formalized communication protocols (CAN, LIN, Ethernet, FlexRay) using OWL + industrial ODPs.
      Integrate with simulation execution platforms to complete the capability-based configuration cycle through automated execution.
      Implement query-driven or rule-based mechanisms to automatically derive capabilities and simulation scenarios from simulation goals.
      Introduce granular, reusable representations of simulation model quality attributes.

## Slide 18
Thank you for your attention!
  —